A REVIEW: NATURAL AND ARTIFICIAL RADIONUCLIDES AND RADIATION HAZARD PARAMETERS IN THE SOIL OF MOUNTAIN REGIONS IN SERBIA

Branislava M. Mitrović1, Dragana Todorović2,

Jelena Ajtić1 and Borjana Vranješ1

1University of Belgrade, Faculty of veterinary medicine,

Bulevar oslobođenja 18, Belgrade, Serbia

2University of Belgrade, Vinča Institute of Nuclear Sciences, Department of Radiation Protection and Environmental Monitoring, Belgrade, Serbia

Abstract: This review paper discusses content of natural (40K, 238U, 226Ra, and 232Th) and artificial (137Cs) radionuclides in the soil of the mountains Maljen, Tara and Kopaonik in the Republic of Serbia over 2002–2015. In addition, the paper gives radiation hazard parameters, i.e., radium equivalent activity, absorbed dose rate, annual effective dose equivalent, external hazard index, annual gonadal dose equivalent, and excess lifetime cancer risk outdoors that we calculated from the obtained content of the natural radionuclides in the soil samples. We compared the parameters to previously published results for different parts of the country and looked into the radioecological status of the investigated areas.

Key words: soil, radionuclides, gamma spectrometry, radiation hazard parameters, mountain region.

Introduction

Ionizing radiation and radioactivity are an integral part of the environment. Natural radionuclides, characterized by a long half-life, are present in rocks, minerals and soil. These primordial terrestrial radionuclides are divided into two groups.

The first group includes three natural decay series, headed by 238U, 232Th and 235U, and their decay products (Atwood, 2010), which are alpha, beta and gamma emitters. In nature, uranium is present as a mixture of 238U (99%, half-life 4.5x109 years), 235U (0.71%, half-life 7.034x108 years), and 234U (0.006%, half-life 2.46x105 years). Thorium-232 (half-life 1.41x1010 years) is less radioactive than uranium but more abundant in nature. The most important radioactive decay isotopes are: 226Ra (half-life 1602 years) that belongs to the 238U series, and 228Ra (half-life 5.7 years) from the 232Th series. A daughter nuclide of 228Ra is a radioactive gas radon, which contributes the largest dose to the radiation from natural radioactive sources.

Radionuclides in the second group are 40K and 87Rb. Potassium-40 (half-life 1.25x109 years) is a radioactive isotope (contributing 0.012%) of potassium that is abundant in nature. Rubidium-87 (half-life 4.88x1010 years) is more abundant in nature (27.83%) than 40K. These two radionuclides present in the soil significantly contribute to the total dose of irradiation to humans and biota (Fisenne, 1993).

An important source of human exposure to radiation is the decay of naturally occurring radionuclides in the soil. Radionuclides are not uniformly distributed; their concentration depends on geographic location, geological origin of the soil, but also anthropogenic activities. All of these factors contribute to the variation of radiation exposure. According to the UNSCEAR report (2008), the average value of worldwide exposure due to the natural radiation sources is 2.4 mSv/y, with a range of 1–10 mS/y. The population receives the highest radiation doses due to the inhalation exposure to 222Rn (1.15 mSv/y), from external terrestrial radiation (0.48 mSv/y), cosmic radiation and cosmogenic radionuclides (0.39 mSv/y), and ingestion of 40K and radionuclides from the uranium and thorium series (0.29 mSv/y).

Materials containing naturally occurring radionuclides and their radioactive decay products that are not disturbed by human activities are called Naturally Occurring Radioactive Material (NORM) (IAEA, 2003). Some activities, such as mining, oil and gas production, coal combustion, use of fertilizers and release of fertilizer production wastes may lead to concentrated NORM materials.

The environmental contamination of Serbia with a fission radionuclide 137Cs (half-life 30 years) is a consequence of the nuclear accident in Chernobyl (in 1986) and nuclear weapons testing in the atmosphere. The 137Cs activity concentration in different regions of the former Republic of Yugoslavia ranged between 1 kBq/m2 and 10 kBq/m2, depending on the prevailing meteorological conditions during the release (EU Commission, 1991). Due to its long half-life, 137Cs can still be found in the environment, especially in the soil and bioindicator organisms, such as mosses, fungi, blueberries and wild animals (Steinnes and Njåstad, 1993; Delfanti et al., 1999; Čučulović et al., 2012; Mitrović et al., 2013b, 2014a, 2016c; Todorović et al., 2013). The retention of 137Cs in the soil depends on the soil physico-chemical characteristics and its clay content, but also on the climate, surrounding vegetation, etc. (Cremers et al., 1988; Rosén et al., 1999; Fujii et al., 2014).

Our paper gives a review of the activity concentration of natural (40K, 238U, 226Ra, and 232Th) and artificial (137Cs) radionuclides in the soil from the mountains of Tara, Maljen and Kopaonik, with an emphasis given to estimating the radiation hazard parameters.

Materials and Methods

The soil samples were collected over 2002–2015 in the areas of the mountains of Maljen, Tara, and Kopaonik (Figure 1). The mountains of Tara and Kopaonik are nature parks and thus all their reserves are under the state protection. The studied areas present some of favorite tourist destinations for sports and recreation.

Figure 1. A view of Serbia with the location of the mountains of Maljen,

Tara and Kopaonik.

The soil samples were collected from the surface down to a depth of 20 cm. In the laboratory, the samples were crushed, dried at 105 °C, sieved, homogenized and put into Marinelli beakers (0.5 ml and 1 l). All samples were hermetically sealed and stored for 21 days to ensure equilibrium between 226Ra and its daughters.

We used gamma-ray spectrometric measurements on High Purity Germanium detectors (ORTEC and Canberra), with a relative efficiency of 18%, 20% and 30%, and an energy resolution 1.85 keV (1332.5 60Co), to determine the activity concentrations of the investigated radionuclides.

The analysis of each measured gamma-ray spectrum was performed by a software program GAMMA VISION-32. All obtained results are expressed as (mean ± standard deviation).

The activity concentrations of 40K and 137Cs were derived directly from their 1460.8 keV and 661.66 keV gamma energies, respectively. For other radionuclides, we included the following steps in the analysis:

- We assumed equilibrium conditions between the parent nuclide 238U and its daughters, 234Th (63.2 keV) and 234mPa (1001 keV).

- We obtained the 226Ra activity concentration from the gamma energy of 186.1 keV corrected for 235U, and 226Ra daughters in equilibrium, 214Bi (609.3 keV, 1120.2 keV and 1764.5 keV) and 214Pb (351.9 keV).

- We used three photo peaks of 228Ac (338 keV, 911.2 keV, and 969 keV) for the activity concentration of 232Th.

Calculation of radiation hazard parameters

Radium equivalent activity

Since the distribution of 226Ra, 232Th, and 40K in the soil is not uniform, we used radium equivalent activity (Raeq) to compare the specific activity of materials with different amounts of 226Ra, 232Th, and 40K. The definition of Raeq is based on an assumption that 370 Bq/kg of 226Ra, 259 Bq/kg of 232Th, and 4810 Bq/kg of 40K produce the same gamma dose rate. We calculated Raeq using (Beretka and Mathew, 1985):

Raeq (Bq/kg) = CRa + 1.43CTh + 0.077CK  							     (1)

where CRa, CTh, and CK are the activity concentrations of 226Ra, 232Th, and 40K (in Bq/kg), respectively.

Absorbed dose rate

We converted the mean activity concentrations of 226Ra, 232Th, and 40K into absorbed dose rate () using conversion factors under an assumption that all decay products of 226Ra and 232Th are in equilibrium with their precursors (UNSCEAR, 2008):

(nGy/h) = 0.462CRa + 0.604CTh + 0.042CK      						(2)

Annual effective dose equivalent

To estimate the annual effective dose equivalent (AEDE), the conversion coefficient from the absorbed dose in the air to the effective dose must be considered. We used the absorbed dose rate data (Eq. 2), adopted the conversion factor of 0.7 Sv/Gy (UNSCEAR, 2008), and assumed that on average, people in Serbia spend 20% of their time outdoors, and thus obtained:

AEDE (µSv/y) =  (nGy/h) x 24 (h) x 365 (days) x 0.7 (Sv/Gy) x 0.2      	(3)

External hazard index

Beretka and Mathew (1985) defined the external hazard index (Hex) as:

Hex = CRa/370 + CTh/259 + CK/4810									(4)

For Hex values less than one, the radiation hazard is insignificant. The external hazard index equal to one corresponds to the upper limit of radium equivalent activity (370 Bq/kg).

Annual gonadal dose equivalent

We used the following equation (Arafa, 2004) to calculate annual gonadal dose equivalent (AGDE) to the population arising from the presence of naturally occurring radionuclides 226Ra, 232Th, and 40K in the soil:

AGDE (µSv/y) = 3.09CRa + 4.18CTh + 0.314CK  						(5)

Excess lifetime cancer risk outdoors

Excess lifetime cancer risk outdoors (ELCRoutdoor) gives the probability of developing cancer over a lifetime at a given exposure level. We calculated ELCRoutdoor using (UNSCEAR, 2000; ICRP, 1990):

ELCRoutdoor = AEDE × DL × Rf										(6)

where DL is the duration of life (70 years average) and Rf is the risk factor (in Sv), i.e. fatal cancer risk per sievert. For stochastic effects, we used Rf = 0.05 mSv for the whole population (ICRP, 2007).

Results and Discussion

Mountains are complex ecological and very sensitive ecosystems. The characteristics of mountain ecosystems vary depending on altitude, climate conditions, geological characteristics, biomes, water flows, etc. Any changes in biotic or abiotic elements can cause an interruption in the ecosystem.

Specific activities of natural radionuclides in the soil depend on geological and geographical characteristics of a given region. In the mountain regions of Maljen, Tara and Kopaonik, serpentine soils are present. Characteristics of this soil type are extremely stressful for plant growth (Kostić et al., 1998; Vicić et al., 2014) – since they are susceptible to erosion, and often shallow and rocky, vegetation is usually sparse and poor (Tatić and Veljović, 1991; Jakovljević et al., 2001; Stevanović et al., 2003).  The geological background of Mt. Kopaonik is represented by granites, serpentinites, slates, marbles, andesites, and limestones. The differences in geological characteristics between the investigated mountains also affect the content of radionuclides in the soil, which will be summarized below.

The presence of anthropogenic radionuclides, such as 137Cs, is mainly a consequence of the nuclear accident in Chernobyl in 1986. The ensuing soil contamination was a result of a number of factors, such as a distance from the accident location, rainfall index, and soil characteristics (UNSCEAR, 2000).

The mountain of Maljen

Maljen is a mountain located in the west of Serbia. It spreads in the east-west direction for approximately 25 km. The highest peak is Kraljev sto (elevation – 1100 m a.s.l.). The geologic structure of Mt. Maljen consists of ultrabasic rocks (peridotites and serpentinized peridotites).  Magnesium oxide present in the soil makes this area unfavorable for plant survival (Tatić and Veljović, 1991).

The soil samples from Mt. Maljen were collected at four altitudes over 2002–2007 (Mitrović et al., 2009). Table 1 gives the gammaspectrometric results.

Table 1. 40K, 238U, 226Ra, 232Th, and 137Cs activity concentrations in the soil collected at Mt. Maljen (Bq/kg)a.

| Altitude (m) | 40K | 238U | 226Ra | 232Th | 137Cs |
| --- | --- | --- | --- | --- | --- |
| 200 | 450 ± 5 | 61 ± 6 | 54 ± 5 | 57 ± 2 | 19 ± 1 |
| 650 | 394 ± 5 | 46 ± 3 | 51 ± 5 | 42 ± 2 | 47 ± 1 |
| 1000 | 70 ± 2 | 11 ± 1 | 11 ± 1 | 8 ± 1 | 64 ± 2 |
| 1100 | 102 ± 1 | 14 ± 1 | 13 ± 1 | 11 ± 1 | 259 ± 1 |
| Average | 254 | 33 | 33 | 29 | 97 |

aMitrović et al. (2009).

The mean activity concentrations of the radionuclides on Mt. Maljen were 254 Bq/kg for 40K, 33 Bq/kg for 238U, 33 Bq/kg for 226Ra, 29 Bq/kg for 232Th, and 97 Bq/kg for 137Cs (Table 1). According to the UNSCEAR report (2000), the world average activity concentrations in the soil are 420 Bq/kg, 33 Bq/kg, 32 Bq/kg, and 45 Bq/kg for 40K, 238U, 226Ra, and 232Th, respectively. Our results showed that the content of natural radionuclides at lower altitudes was above the world average values. However, as altitude increased, the activity of natural radionuclides in the soil decreased by a factor of 4–6. This finding can be explained by different geochemical characteristics of the soil at different altitudes, and by the fact that soils in lower areas are generally subject to agro-technical measures and use of fertilizers based on phosphate and potassium (Bolca et al., 2007).

In contrast to this finding, there was a several-fold increase in the 137Cs activity concentration from an altitude of 200 m (19 Bq/kg) to 1100 m (259 Bq/kg), which could be explained by an increased amount of rainfall at higher altitudes after the Chernobyl accident. Contamination of the soil with 137Cs is a starting point for transfer of this radionuclide to plants and onwards through the food chain. Its presence was detected in mosses, mushrooms, game meat and milk of animals from the test sites (Mitrović et al., 2009). The highest content of 137Cs was found in sheep meat (45.8 Bq/kg) and goat milk (24.1 Bq/kg) sampled from animals grazing at 1000 m a.s.l.

Based on the measured activity concentrations of natural radionuclides in the soil (Table 1), we calculated radiation hazard parameters for Mt. Maljen (Table 2). The radium equivalent activity was below 170 Bq/kg (Table 2). For comparison, a value of 370 Bq/kg is the criterion limit for Raeq in building materials (Beretka and Mathew, 1985), and its corresponding annual effective dose equivalent is 1 mSv, which, in turn, represents the dose limit for the general population. Further, the locations at lower altitudes showed an absorbed dose rate higher than the world average of 59 nGy/h (UNSCEAR, 2008). The calculated annual effective dose equivalents at lower altitudes were also higher than the world mean of 70 µSv/y (UNSCEAR, 2000), while the annual gonadal dose equivalent values were lower than the level of 1 mSv/y, which is a recommended limit by the International Commission on Radiological Protection (2007) for the general public. According to UNSCEAR (2000), the gonads, bone marrow, and bone surface are considered as the organs of importance since they are active. The probability of cancer incidence in a population during the lifetime due to an exposure to natural radionuclides (ELCRoutdoor) in the soil at lower altitudes was slightly higher than the world average value of 0.29x10-3 (UNSCEAR, 2000), but the mean ELCRoutdoor value was lower (0.20x10-3).

Table 2. Radiation hazard parameters for the soil collected at Mt. Maljen.

| Altitude (m) | Raeq (Bq/kg) | (nGy/h) | AEDE (µS/y) | Hex | AGDE (µSv/y) | ELCRoutdoor x10-3 |
| --- | --- | --- | --- | --- | --- | --- |
| 200 | 169 | 78 | 95 | 0.46 | 544 | 0.36 |
| 650 | 141 | 65 | 80 | 0.38 | 455 | 0.30 |
| 1000 | 27 | 13 | 16 | 0.07 | 88 | 0.06 |
| 1100 | 37 | 17 | 21 | 0.10 | 120 | 0.08 |
| Average | 94 | 43 | 53 | 0.25 | 302 | 0.20 |
| Average world values | 370a | 59b | 70c | ≤ 1d | 1000e | 0.29 x10-3)f |

aBeretka and Mathew (1985); bUNSCEAR (2008); cUNSCEAR (2000); dICRP (2000); eICRP (2007); fUNSCEAR (2000).

As a summary of the above results, the obtained external hazard index for altitudes above 200 m was less than one (Table 2), i.e., less than the limit recommended by ICRP (2000), implying that the investigated area is radioecologically safe to use.

The mountain of Tara

Farther west and south from Maljen is the mountain of Tara. It covers an area of 250 km2 and geologically belongs to the Dinarides. The highest peak is Kozji rid (1591 m a.s.l.). The climate is distinctly mountainous, and the winter period is cold with plenty of snow. The soil is mainly uncultivated, dominated by the forest ecosystem (80%). The soil is composed of various limestones (MgCO3, CaCO3) and shale (Si) rocks. Forests mainly consist of beech, spruce and fir.

Table 3 gives the activity concentrations of radionuclides in the soil of Mt. Tara, while Table 4 shows the calculated radiation hazard parameters. In all soil samples, the activity concentrations of natural radionuclides were below the world average (Table 3), except the altitude of 1100 m where the content of 238U, 226Ra, and 232Th was higher (Djurić et al., 1996; Mitrović et al., 2009; Rakić et al., 2014). The obtained results showed that the level of natural radionuclides’ activity in non-cultivated soil of the mountains of Maljen and Tara was similar (Tables 1 and 3). Popović et al. (2009) reported that the mean activities of 226Ra, 232Th, and 40K in the soil from Mt. Tara collected over a period of 1983–1993 were 42 Bq/kg (22–92 Bq/kg), 46 Bq/kg (24–69 Bq/kg) and 613 Bq/kg (356–1126 Bq/kg), respectively. Differences in radionuclides’ content in the soil are a consequence of soil type. For example, higher activity concentrations of 40K, 238U, and 232Th can be found in shale soils than in the soil composed mainly of limestone rocks (Djurić et al., 1996).

Table 3. 40K, 238U, 226Ra, 232Th and 137Cs activity concentrations in the soil collected at Mt. Tara (Bq/kg).

| Altitude (m) | 40K | 238U | 226Ra | 232Th | 137Cs | Reference |
| --- | --- | --- | --- | --- | --- | --- |
| 300 | 420 ± 25 | 34 ± 3 | / | 43 ± 3 | / | Djurić et al. (1996) |
| 1000 | 72 ± 3 | 11 ± 1 | 11 ± 1 | 8.3 ± 0.4 | 91 ± 4 | Mitrović et al. (2009) |
| 1000 | 368 ± 37 | 30 ± 2 | / | 31 ± 3 | / | Djurić et al. (1996) |
| 1082 (Site 1) | 143 ± 10 | / | 23 ± 3 | / | 221 ± 6 | Rakić et al. (2014) |
| 1082 (Site 2) | 237 ± 10 | / | 14 ± 1 | / | 189 ± 6 | Rakić et al. (2014) |
| 1100 | 395 ±11 | 50 ± 5 | 50 ± 5 | 49 ± 2 | 104 ± 8 | Mitrović et al. (2009) |
| Average | 300 | 31 | 31 | 30 | 98 |  |

The values of radiation hazard parameters on all sample locations were below the recommended maximum values (Tables 2 and 4). The exception again was the soil collected at 1100 m a.s.l. where absorbed dose rate (), annual effective dose equivalent (AEDE) and excess lifetime cancer risk (ELCRoutdoor) were about 1.2-fold higher than the recommended levels.

Table 4. Radiation hazard parameters for the soil collected at Mt. Tara.

| Altitude (m) | Raeq (Bq/kg) | (nGy/h) | AEDE (µSv/y) | Hex | AGDE (µSv/y1) | ELCRoutdoorx10-3 |
| --- | --- | --- | --- | --- | --- | --- |
| 1000 | 28 | 13 | 16 | 0.08 | 91 | 0.06 |
| 1100 | 150 | 69 | 85 | 0.41 | 483 | 0.32 |
| Average | 89 | 41 | 51 | 0.24 | 287 | 0.19 |

Anthropogenic 137Cs was also detected in the soil (Table 3). In 1991, five years after the Chernobyl accident, the activity concentration of this radionuclide in the surface layers was significantly lower in limestone soils (88 Bq/kg) than in shale soils (462 Bq/kg) (Djurić et al., 1996; Popović et al., 1996; Popović and Spasić, 2006; Popović et al., 2009), and it is still present in the soil (Rakić et al., 2014).

Transfer of this radioisotope from the soil to plants strongly depends on the soil type and characteristics of the plant species. The study by Mitrović et al. (2009) showed that radiocesium was present in the food chain: soil-plants-animals. Between 2002 and 2007, the medium activity concentration of 137Cs was 5.1 Bq/kg in the grass, 2.9 Bq/kg in sheep milk, and 6.5 Bq/kg in sheep meat. Small ruminants, such as sheep and goats, are good bioindicators for radiocesium contamination of the environment, because the ingestion of soil can be a major source of radiocontamination for free-grazing ruminants (Assimakopoulos et al., 1993).

After the Chernobyl accident, the activity concentrations of 134Cs and 137Cs in herbal teas from Serbia reached 5000 Bq/kg (Petrović, 2010), but results obtained 28 years later showed a significant reduction in the 137Cs concentration in teas from mountain regions (Mitrović et al., 2014).  In herbal teas collected from Mts Maljen and Tara, high activity concentrations of 137Cs (77 Bq/kg and 73 Bq/kg, respectively) were observed in plant species V. myrtillus (bilberry). Some organisms, e.g. bilberry but also mosses, mushrooms and game, are good bioindicators of environmental pollution with radiocesium (Grdović et al., 2010; Mitrović et al., 2013, 2016a,b; Rakić et al., 2014).

The mountain of Kopaonik

The south-western part of Serbia is dominated by Kopaonik, which is one of the highest mountain ranges in the country. It extends in the northwest-southeast direction for 80 km, and has a width of around 40 km in the middle. The highest peak is Pančićev vrh (elevation – 2017 m a.s.l.). The Kopaonik National Park covers an area of about 12000 ha, and it is a very popular tourist destination. The climate is subalpine with the annual average precipitation rate up to 1000 mm.

The results of gamma spectrometric determination of radionuclides in the soil collected on nine locations at Mt. Kopaonik during 2013–2016 (Mitrović et al., 2014, 2016; Džoljić et al., 2017) and radiation hazard parameters are presented in Tables 5 and 6, respectively.

The mean activity concentrations of radionuclides at Mt. Kopaonik were 723 Bq/kg for 40K, 78  Bq/kg for 238U, 75 Bq/kg for 226Ra, and 76  Bq/kg for  232Th (Table 5), which is two-fold higher than the world average activity concentrations of these radionuclides in the soil (UNSCEAR, 2000). The obtained differences between the results can be attributed to the geological structure at the sampling locations. For example, at Lisina, a sampling site with an elevation of 1300 m, the geological period belongs to the Palaeozoic, and rocks are comprised of granite, granodiorite and quartz, known for its high content of radionuclides. On the other hand, higher up at Gobelja, metamorphic rocks (crystalline shales) are found. Furthermore, the results showed an increase of natural radionuclides 238U, 226Ra, and 232Th with altitude. An exception was the Đerekare location where somewhat higher radionuclide content was detected.

Table 5. 40K, 238U, 226Ra, 232Th and 137Cs activity concentrations in the soil collected at Mt. Kopaonik (Bq/kg).

| Sampling site | Altitude (m) | 40K | 238U | 226Ra | 232Th | 137Cs |
| --- | --- | --- | --- | --- | --- | --- |
| Brusa | 429 | 526 ± 16 | 27 ± 4 | 29 ± 2 | 32 ± 2 | 31 ± 1 |
| Jošanička banjaa | 557 | 269 ± 8 | 33 ± 4 | 29 ± 3 | 32 ± 6 | 142 ± 4 |
| Đerekarea | 950 | 920 ± 27 | 70 ± 6 | 78 ± 6 | 89 ± 7 | 6.0 ± 0.2 |
| Brzećea | 980 | 620 ± 19 | 33 ± 5 | 34 ± 4 | 36 ± 3 | 32 ± 1 |
| Brezećeb | 1100 | 650 ± 40 | 37 ± 5 | 30 ± 3 | 41 ± 3 | 89 ± 5 |
| Lisinaa | 1300 | 730 ± 21 | 184 ± 10 | 174 ± 10 | 133 ± 5 | 79 ± 2 |
| Suvo Rudišteb | 1700 | 780 ± 50 | 93 + 8 | 88 ± 6 | 111 ± 7 | 9.8 ± 0.8 |
| Gobeljaa | 1934 | 722 ± 21 | 62 ± 5 | 65 ± 4 | 63 ± 2 | 30 ± 1 |
| Pančićev vrha | 2017 | 1291 ± 39 | 160 ± 10 | 152 ± 11 | 151 ± 9 | 4.2 ± 0.2 |
| Average |  | 723 | 78 | 75 | 76 | 47 |

aMitrović et al. (2016); bDžoljić et al. (2017).

Mt. Kopaonik was under a prolonged attack during the NATO action against the Federal Republic of Yugoslavia in 1999.  The bombing led to the destruction of the terrain and disruption of the forest ecosystem (UNEP/UNCHS BTF, 1999). The gammaspectrometric analysis of the soil taken from the Gobelja location where severe bombing activity took place, showed that activity concentrations of 238U and 226Ra were in equilibrium, implying a natural origin of the radionuclides (Mitrović et al., 2016). This study, however, did not investigate soil samples from the bombing craters. The average activity concentration of 137Cs (47 Bq/kg) on Mt. Kopaonik was two-fold lower than on Mt. Maljen (97 Bq/kg) and Mt. Tara (98 Bq/kg). These variations can be explained by a different deposition of Chernobyl radiocesium, differences in forest type (Koarashi et al., 2016), physical and chemical properties of soils (Korashi et al., 2012), as well as the sedimentary structure of this location (Mitrović et al., 2016).

The radium equivalent activity in the soil was mostly below 370 Bq/kg (Table 6). The exceptions were the locations of Lisina and Pančićev vrh where Raeq exceeded this limit (415 Bq/kg and 458 Bq/kg, respectively). As a consequence of the high activity concentration of natural radionuclides in the soil, the values of absorbed dose rate () and annual effective dose equivalent (AEDE) were higher than the global average of 58 nGy/h (UNSCEAR, 2008) and 70 µSv/y (UNSCEAR, 2000), respectively. However, at lower altitudes, in Brus and Jošanička banja, these two parameters were below the global means (Table 6).

Table 6. Radiation hazard parameters for the soil collected in Mt. Kopaonik.

| Sampling site | Altitude (m) | Raeq (Bq/kg) | (nGy/h) | AEDE (µSv/y) | Hex | AGDE (µSv/y) | ELCRoutdoorx10-3 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Brusa | 429 | 115 | 55 | 67 | 0.31 | 389 | 0.25 |
| Jošanička banjaa | 557 | 95 | 44 | 54 | 0.26 | 308 | 0.20 |
| Đerekarea | 950 | 276 | 128 | 158 | 0.75 | 902 | 0.59 |
| Brzećea | 980 | 133 | 63 | 78 | 0.36 | 450 | 0.29 |
| Brezećeb | 1100 | 139 | 66 | 81 | 0.37 | 468 | 0.31 |
| Lisinaa | 1300 | 420 | 191 | 235 | 1.14 | 1323 | 0.89 |
| Suvo Rudišteb | 1700 | 307 | 140 | 172 | 0.83 | 981 | 0.65 |
| Gobeljaa | 1934 | 211 | 98 | 121 | 0.57 | 691 | 0.46 |
| Pančićev vrha | 2017 | 467 | 216 | 264 | 1.26 | 1506 | 1.00 |
| Average |  | 240 | 111 | 137 | 0.65 | 780 | 0.52 |

aMitrović et al. (2016); bDžoljić et al. (2017).

In all locations except Lisina and Pančićev vrh, the annual gonadal dose equivalent (AGDE) values were lower than 1 mSv/y. Similarly, the average value for the external hazard index (Hex) was less than one (Table 6). Still, values higher than 1 were recorded in Lisina and Pančićev vrh. The probability of cancer incidence in a population during the lifetime due to an exposure to natural radionuclides in the soil (ELCRoutdoor) at higher altitudes was higher than the world average value of 0.29x10-3 (UNSCEAR, 2000).

In addition to the natural radionuclides, the artificial 137Cs was detected in the soil, grass, spruce, cow milk and moss samples from Mt. Kopaonik (Mitrović et al., 2016; Džoljić et al., 2017). In the soil, the lowest activity concentration of 137Cs was recorded in the area of Pančićev vrh, and the maximum in Jošanjička banja (Table 5). A decrease in the 137Cs content in the soil with an increasing altitude is probably due to stronger soil erosion at higher altitudes (Nešić et al., 2009).

Radionuclides in the soil of Serbia

Determination of radionuclides’ content in the soil has been a subject of many studies with the purpose of risk assessment and protection of the humans, non-human biota and the environment from radioactive pollution. Studies performed by Momčilović et al. (2010) and Tanič et al. (2014) in the area of an abandoned uranium mine (Grabovnica mine) at Mt. Stara Planina showed that the terrestrial gamma dose rate due to 238U (31–237 Bq/kg), 232Th (6–109 Bq/kg), and 40K (64–977 Bq/kg) in the soil was two-fold higher than that of the surrounding area. In the vicinity of the mine compounds, the radionuclide content was within the usual range for this mountain or slightly higher.  In a part of Mt. Stara Planina farther south, at sampling points of Smilovci, Smilovsko jezero, Kamenica, and Gornji Krivodol, the activity concentrations of natural radionuclides in the soil were lower and ranged between 393 Bq/kg and 543 Bq/kg, 29 Bq/kg and 57 Bq/kg, 25 Bq/kg and 51 Bq/kg, and 28 Bq/kg and 69 Bq/kg for 40K, 238U, 226Ra, and 232Th, respectively (Vranješ et al., 2016). Apart from the natural radionuclides, 137Cs was also detected in the environment of Mt. Stara Planina, i.e. in the soil, mosses and medicinal plants (Vranješ et al., 2016).

Gammaspectrometric determination of radionuclides present in the soil from Mt. Zlatibor (Dragović et al., 2010a) showed that the content of 40K ranged between 212 Bq/kg and 740 Bq/kg, 238U between 10.6 Bq/kg and 69.0 Bq/kg, 226Ra between 8.3 Bq/kg and 87.5 Bq/kg, 232Th between 10.4 Bq/kg and 41.4 Bq/kg, and 137Cs between 73 Bq/kg and 155 Bq/kg. This study showed enrichment of 226Ra with respect to 238U in some soil samples, probably due to greater mobility of uranium, which, in turn, led to a depleted content of this element relative to radium. In Mt. Zlatibor, anthropogenic 137Cs was detected in bioindicators, as well as ants, mosses, lichens (Dragović et al., 2010a,b) and medicinal plants (Mitrović et al., 2013, 2014, 2016).

Investigation of radionuclide content in the soil has also been conducted in urban areas (Grdović et al., 2010; Janković Mandić and Dragović, 2010; Dragović et al., 2012; Milenković et al., 2015; Mitrović et al., 2016b; Vukašinović et al., 2018), agriculture soil (Vukašinović et al., 2009, 2010; Bikit et al., 2011; Mitrović et al., 2013b; Forkapić et al., 2017) and in the vicinity of industrial plants (Vitorović et al., 2012; Vukašinović et al., 2014). Gammaspectrometric determination of 238U in the soil sampled from 21 different locations in Serbia and Montenegro showed that uranium content ranged from 1.28 ppm on Slatina (approximately 15.7 Bq/kg) to 4.80 ppm in Vranje (approximately 58.8 Bq/kg), with the mean value of 2.76 ppm (approximately 33.8 Bq/kg) (Dragović et al., 2006b). The absorbed gamma dose rates () ranged between 24.5 nGy/h and 97.6 nGy/h, with the mean of 66.8 nGy/h, annual effective dose equivalent (AEDE) varied from 42.3 µSv/y to 119 µSv/y, with the mean of 81.9 µSv/y (Dragović et al., 2006a); and the radiation hazard was insignificant for population living in the investigated areas.

It is also worth noting that many studies have been conducted to determine the uranium content in various environmental samples from locations where depleted uranium ammunition was used during the NATO bombing in 1999 (Miljević et al., 2001; Esposito et al., 2002; Popović et al., 2008, 2010; Sarap et al., 2014). These locations are now included as an integral part of the monitoring program at the territory of the Republic of Serbia (Official Gazette RS, 2010).

Conclusion

Determining natural radioactivity in the soil is a necessary step in the evaluation of the radiation hazard parameters. The average values of activity concentrations of 238U, 226Ra and 232Th at Mts Maljen and Tara were within the range of values obtained for other parts of Serbia and worldwide (UNSCEAR, 2008). However, the measured concentrations were approximately two-fold higher at Mt. Kopaonik.

The radiation hazard parameters obtained for Mts Maljen and Tara were similar to values reported for other parts of Serbia implying that the investigated areas were radioecologically safe for humans.

Mt. Kopaonik showed the average values of absorbed dose rate, annual effective dose equivalent and external hazard index two-fold higher than at Mts Maljen and Tara. At two particular locations, Lisina and Pančićev vrh, the values of absorbed dose rate and annual effective dose equivalent were about four-fold higher than those on Mts Maljen and Tara. External hazard index was also higher than one, indicating an elevated radiation hazard.

The values of annual gonadal dose equivalent, as a measure of the genetic significance of the annual dose equivalent received by the population, were less than 1 mSv in the investigated areas, except on Mt. Kopaonik, locations Lisina and Pančićev vrh, where this parameter was higher than 1 mSv.

The calculated excess lifetime cancer risk implied that the chance of contracting cancer for residents at the study area of Mts Maljen and Tara was below the global average of 0.29x10-3 (UNSCEAR, 2000). However, the probability of cancer incidence on Mt. Kopaonik was higher than the world average.

Anthropogenic 137Cs was detected in all investigated mountain regions of Serbia.

Acknowledgements

This paper is a part of the research done within the projects financed by the Ministry of Education, Science and Technological Development of the Republic of Serbia (TR31003 and TR34013, and III43007) (2011–2019).

References

Arafa, W. (2004). Specific activity and hazards of granite samples collected from the Eastern Desert of Egypt. Journal of Environmental Radioactivity, 75, 315-327.

Assimakopoulos, P.A., Ioannides, K.G., Karamanis, D.T., Pakou, A.A., Stamoulis, K.C., Mantzios, A.S., & Nikolaou, E. (1993). Radiocaesium transfer to sheep’s milk as a result of soil ingestion. Science of the Total Environment, 136, 13-24.

Atwood, D.A. (2010). Radionuclides in the Environment. Willey, 2010.

Beretka, J., & Mathew, P.J. (1985). Natural radioactivity of Australian building materials, industrial wastes and by-products. Health Physics, 48 (1), 87-95.

Bikit, I., Forkapić, S., Nikolov, J., Todorović, N., & Mrdja, D. (2011). Radioactivity of the Agricultural Soil in Northern Province of Serbia, Vojvodina. International Journal of Environmental and Ecological Engineering, 5 (4), 298-303.

Bolca, M., Sac, M., Cokuysal, B., Karali, T., & Ekdal, E. (2007). Radioactivity in soils and various foodstuffs from the Gediz river basin of Turkey. Radiation Measurements, 42, 263-270.

Cremers, A., Elsen, A., De Preter, P., & Maes, A. (1988). Quantitative analysis of radiocaesium retention in soils. Nature, 335, 247-249.

Čučulović, A., Popović, D., Čučulović, R., & Ajtić, J. (2012). Natural radionuclides and 137Cs in moss and lichen in Eastern Serbia. Nuclear Technology and Radiation Protection, 27 (1), 44-51.

Delfanti, R., Papucci, C., & Benco, C. (1999). Mosses as indicators of radioactivity deposition around a coal-fired power station. Science of the Total Environment, 227 (1), 49-56.

Dragović, S., Janković, Lj., & Onjia, A. (2006a). Assessment of gamma dose rates from terrestrial exposure in Serbia and Montenegro. Radiation Protection Dosimetry, 121, 297-302.

Dragović, S., Janković, L., Onjia, A., & Bačić, G. (2006b). Distribution of primordial radionuclides in surface soils from Serbia and Montenegro. Radiation Measurements, 41, 611-616.

Dragović, S., Mihailović, N., & Gajić, B. (2010a). Quantification of transfer of 238U, 226Ra, 232Th, 40K and 137Cs in mosses of a semi-natural ecosystem. Journal of Environmental Radioactivity, 101, 159-164.

Dragović, S., Howard, B.J., Caborn, J.A., Barnett, C.L., & Mihailović, N. (2010b). Transfer of natural and anthropogenic radionuclides to ants, bryophytes and lichen in a semi-natural ecosystem. Environmental Monitoring and Assessment, 166, 677-686.

Dragović, S., Gajić, B., Dragović, R., Janković-Mandić, L., Slavković-Beškoski, L., Mihailović, N., Momčilović, M., & Ćujić, M. (2012). Edaphic factors affecting the vertical distribution of radionuclides in the different soil types of Belgrade, Serbia. Journal of Environmental Monitoring, 14, 127-137.

Djuric, G., Popovic, D., & Todorovic, D. (1996). Activity variations and concentration factors for natural radionuclides in a “soil-plant-honey” system. Environment International, 22, 361-363.

Džoljić, A.J., Stevović, M.S., Todorović, J.D., Polavder, M.S., Rajačić, M.M., & Krneta Nikolić, N.J. (2017). Natural and artificial radioactivity in some protected areas of south east Europe. Nuclear Technology and Radiation Protection, 32, 334-341.

Esposito, M., Polić, P., Bartolomei, P., Benzi, V., Martellini, M., Cvetković, O., Damjanov, V., Simić, M., Žunić, Z., Živančević, B., Simić, S., & Jovanović, V. (2002). Survey of natural and anthropogenic radioactivity in environmental samples from Yugoslavia. Journal of Environmental Radioactivity, 61, 271-282.

EU Commission. (1991). Radioactivity measurement in Europe after the Chernobyl accident, Part Fallout and deposition, Radiation protection. EUR Report 12800. Commission of the European Communities, Brussels – Luxemburg.

Fisenne, M. (1993). Long lived radionuclides in the Environment, in Food and Human Beings, in: CEC Report on Natural Radiation Environment, EUR 14411, EN, Luxemburg, pp. 187-260.

Forkapić, S., Vasin, J., Bikit, I., Mrdja, D., Bikit, K., & Milić, S. (2017). Correlations between soil characteristics and radioactivity content of Vojvodina soil. Journal of Environmental Radioactivity, 166, 104-111.

Fujii, K., Ikeda, S., Akama, A., Komatsu, M. Takahashi, M., & Kaneko S. (2014). Vertical migration of radiocesium and clay mineral composition in five forest soils contaminated by the Fukushima nuclear accident. Soil Science and Plant Nutrition, 60, 751-764.

Grdović, S., Vitorović, G., Mitrović, B., Andrić, V., Petrujkić, B., & Obradović, M., (2010). Natural and anthropogenic radioactivity of feedstuffs, mosses and soil in the Belgrade environment. Serbian Archive of Biological Science, 62, 301-307.

Grupa autora, (1970). Osnovna geološka karta SFRJ, list Novi Pazar 1:100 000. Savezni geološki zavod, Beograd.

International Atomic Energy Agency, (IAEA) (2003). Extent of environmental contamination by natural occurring radioactive materials (NORM) and technological options for mitigation. TRS No. 419, IAEA, Wienne.

International Commission on Radiological Protection, ICRP (1990). Recommendations of the international commission on radiological protection, Vol. 21. No:1-3 Publication 60.

International Commission on Radiological Protection, (ICRP) (2000). Protection of the public in situations of prolonged radiation exposure. ICRP Publication 82, Ann. ICRP, 29(1–2).

International Commission on Radiological Protection, ICRP (2007) Recommendations of the International Commission on Radiological Protection, vol. 37, ICRP Publication 103.

Jakovljević, K., Lakušić, D., Vukojičić, S., Tomović, G., Šinžar-Sekulić, J., & Stevanović, V. (2011). Richness and diversity of Pontic flora on serpentine of Serbia. Central European Journal of Biology, 6, 260-274.

Janković Mandić, Lj., & Dragović, S. (2010). Assessment of terrestrial gamma exposure to the population of Belgrade (Serbia). Radiation Protection Dosimetry, 140, 369-377.

Koarashi, J., Atarashi-Andoh, M., Matsunaga, T., & Sanada, Y. (2016). Forest type effects on the retention of radiocesium in organic layers of forest ecosystems affected by the Fukushima nuclear accident. Scientific Reports, 6, 1-11.

Koarashi, J., Moriya, K., Atarashi-Andoh, M., Matsunaga, T., Fujita, H., & Nagaoka, M. (2012). Retention of potentially mobile radiocesium in forest surface soils affected by the Fukushima nuclear accident. Scientific Reports, 2, 2-6.

Kostić, N., Wilson, J.M., Živković, M., & Bain, D. (1998). Mineralogy and geochemical speciation of heavy metals in some serpentine soils of Serbia. In: 16th World Congress of Soil Science, Montpellier, August 20-26, 1998. Elsevier, Amsterdam, pp 444-455.

Milenković, B., Stajić, J.M., Gulan, L., Zeremski, T., & Nikezić, D. (2015). Radioactivity levels and heavy metals in the urban soil of Central Serbia. Environmental Science and Pollution Research, 22, 16732-16741.

Miljević, N.R., Marković, M.M., Todorović, D.J., Cvijović, M.R., Golobočanin, D.D., Orlić, M.P., Veselinović, D.S., & Biočanin, R.N. (2001). Uranium content in the soil of the Federal Republic of Yugoslavia after NATO intervention. Archive of Oncology, 9, 245-249.

Mitrović, B., Vitorović, G., Vitorović, D., Pantelić, G., & Adamović, I. (2009). Natural and anthropogenic radioactivity in the environment of mountain region of Serbia. Journal of environmental monitoring, 11, 383-388.

Mitrović, B., Vitorović, G., Pantelić, G., Vitorović, D., Andrić, V., & Grdović, S. (2013a). Aktivnost 137Cs i 40K u lekovitom bilju sa područja Zlatibora. Zbornik Radova, XXVII simpozijum Društva za zaštitu od zračenja Srbije i Crne Gore, Vrnjačka Banja, 2.10.-4.10.2013., 61-64.

Mitrović, B., Vitorović, G., Andrić, V., Stojanović, M., Vitorović, D., Grdović, S., & Vićentijević, M. (2013b). Prirodni radionuklidi u mineralnim đubrivima i obradivom zemljištu. Veterinarski glasnik, 67 (5-6), 301-464.

Mitrović, B.M., Grdović, S.N., Vitorović, G.S., Vitorović, D.P., Pantelić, G.K., & Grubić G.A. (2014a). 137 Cs and 40 K in some traditional herbal teas collected in the mountain regions of Serbia. Isotopes in Environmental and Health Studies, 50, 538-545.

Mitrović, B., Vitorović, G., & Lazić, M. (2014b). Specifična aktivnost 40K i 137cs u uzorcima zemlje, sena, mahovine i mleka prikupljenih sa područja Kopaonika. Veterinarski žurnal Republike Srpske, 14 (1), 55-62.

Mitrović, B., Ajtić, J., Lazić, M., Andrić, V., Krstić, N., Vranješ, B., & Vićentijević, M. (2016a). Natural and anthropogenic radioactivity in the environment of Kopaonik mountain, Serbia. Environmental Pollution, 215, 273-279.

Mitrović, B., Grdović, S., Vranješ, B., Vićentijević, M., Ajtić, J., & Sarvan, D. (2016b). Radioecological investigation in the environment of Belgrade city, Serbia. Radiation & Applications, online, pp. 199-203. doi: 10.21175/RadJ.2016.03.037

Mitrović, B., Ajtić, J., Grdović, S., Andrić, V., Lazić, M., & Vranješ, B. (2016c). Radiocezijum u životnoj sredini planinskih regiona na teritoriji Republike Srbije. Monografija Černobilj 30 godina posle. Institut za nuklearne nauke „Vinča”, Laboratorija za zaštitu životne sredine „Zaštita” i Društvo za zaštitu od zračenja Srbije i Crne Gore. Beograd, 2016, 127-135. ISBN 978-86-7306-138-2

Mitrović, B. (2019). Radioekološka ispitivanja na podurčju opštine Lazarevac. Zbornik radova „Rudarstvo 2019“, 10. simpozijum sa međunarodnim učešćem, Bor, 28-31.maj 2019, pp. 56-65.

Momčilović, M., Kovačević, J., & Dragović, S. (2010). Population doses from terrestrial exposure in the vicinity of abandoned uranium mines in Serbia. Radiation Measurements, 45, 225-230.

Nešić, D., Belij, S., & Milovanović, B. (2009). Mechanism of genesis of sliding block fields on the south slope of Pančić’s peak (2017 m), Kopaonik. Bulletin of the Serbian geographical society, 89, 37-59.

Official Gazette RS (2010). Rulebook for Establishing Programme of Systematic Environmental Radioactivity Examination, 100/10 from 28.12.2010.

Petrović, L. (2010). Nuclear incident in Chernobyl 1986 – an addition to the research of the environmental problems of the 20th century. History of the 20th Century, 28, 101-116

Popović, D., Djurić, G. & Todorović, D. (1996). Chernobyl fallout radionuclides in soil, plant and honey of a mountain region. International Conference "A Decade after Chernobyl", Vienna, IAEA Tech. Reports, 964 (2), 432-437.

Popović, D., & Spasić-Jokić, V. (2006). Consequences of Chernobyl disaster in the region of the Republic of Serbia. Vojnosanitetski pregled, 63, 481-487.

Popović, D., Todorović, D., Frontasyeva, M., Ajtić, J., Tasić, M., & Rajšić, S. (2008). Radionuclides and heavy metals in Borovac, Southern Serbia. Environmental Science and Pollution Research international, 15, 509-520.

Popović, D., Todorović, D., Jokić, V.S., Nikolić, J., & Ajtić, J. (2009). Contents of radionuclides in soils in Serbia: Dose calculations and environmental risk assessment. Advances in Environmental Research, 6, 91-134.

Popović, D., Bozić, T., Stevanović, J., Frontasyeva, M., Todorović, D., Ajtić, J., & Jokić, V.S. (2010). Concentration of trace elements in blood and feed of homebred animals in Southern Serbia. Environmental Science and Pollution Research, 17, 1119-1128.

Rakić, M., Karaman, M., Forkapić, S., Hansman, J., Kebert, M., Bikit K., & Mrdja, D. (2014). Radionuclides in some edible and medicinal macrofungal species from Tara Mountain, Serbia. Environmental science and pollution research international, 21, 11283-11292.

Rosén, K., Öborn, I., & Lönsjö, H. (1999). Migration of radiocaesium in Swedish soil profiles after the Chernobyl accident, 1987–1995. Journal of Environmental Radioactivity, 46, 45-66.

Sarap, N.B., Janković, M.M., Todorović, D.J., Nikolić, J.D., & Kovačević, M.S. (2014). Environmental radioactivity in southern Serbia at locations where depleted uranium was used. Arhiv za Higijenu Rada i Toksikologiju, 65, 189-197.

Steinnes, E., & Njåstad, O. (1993). Use of mosses and lichens for regional mapping of 137Cs fallout from the Chernobyl accident. Journal of Environmental Radioactivity, 21 (1), 65-73.

Stevanović, V., Tan, K., & Iatrou, G. (2003). Distribution of the endemic Balkan flora on serpentine I. Obligate serpentine endemics. Plant Systematics and Evolution, 242, 149-170.

Tanić, M.N., Momčilović, M.Z., Kovačević, J.R., Dragović, S.D., Bačić, G.G., Tanic, M., Momcilovic, M., Kovacevic, J., Dragovic, S., & Bacic, G. (2014). Assessment of radiation exposure around abandoned uranium mining area of Stara Planina Mt. Serbia. Nuclear Technology and Radiation Protection, 29, 58-66.

Tatić, B., & Veljović, V. (1991). Distribution of serpentinized missives on the Balkan peninsula and their ecology. In: The ecology of areas with serpentinized rocks. Ed: Roberts BA. Proctor J. Springer Netherlands; 1991. p. 199-215.

Todorović, D., Popović, D., Ajtić, J., & Nikolić, J. (2013). Leaves of higher plants as biomonitors of radionuclides (137Cs, 40K, 210Pb and 7Be) in urban air. Environmental Science and Pollution Research, 20 (1), 525-532.

UNEP/UNCHS Balkans Task Force (BTF), 1999. Assessment of the damage to biodiversity in protected areas of the Federal Republic of Yugoslavia. Available online. http://www.grid.unep.ch/btf/missions/september/biodiversity.pdf

United Nations Scientific Committee on the Effects of Atomic Radiation (UNSCEAR), 2000. Sources and Effects of Ionizing Radiations. Report to General Assembly with Scientific Annexes, United Nations, New York.

United Nations Scientific Committee on the Effects of Atomic Radiation (UNSCEAR), 2008. Sources and Effect of Ionizing Radiation. Annex B. United Nation Publications, New York.

Vitorović, G.S, Mitrović, M.B., Andrić, D.V., Stojanović, D.M., Lazarević-Macanović, V.M., & Vitorović, P.D. (2012). Radioactive contamination of food chain around coal mine and coal-fired power stations. Nuclear Technology and Radiation Protection, 27, 388-391.

Vranješ, B., Mitrović, B., Andrić, V., & Grdović, S. (2016). Radioactivity in environment of Stara Planina Mountain in area of summer school for mountain animal breeding. Book of Abstracts. Fourth International Conference on Radiation and Applications in Various Fields of Research, May 23-27, Niš, Serbia. ISBN: 978-86-6125-160-3

Vukašinović, I., Todorović, D., Dordević, A., Rajković, M.B., Stojanović, M., & Pavlović, V.B. (2009). Natural isotopes 238U and 40K content in rigosol from the area of school estate good „Radmilovac” of Faculty of Agriculture, Zemun. Journal of Agricultural Science, 54 (2), 143-151.

Vukašinović, I., Dordević, A., Rajković, M.B., Todorović, D., & Pavlović, V.B. (2010). Distribution of natural radionuclides in anthrosol-type soil. Turkish Journal of Agriculture and Forestry, 34, 539-546.

Vukašinović, I., Todorović, D., Mihajlović, A., & Eremić, M., (2014). Radioactivity measurements in soils surrounding four coal-fired power plants in Serbia by gamma-ray spectrometry and estimated dose. Nuclear Technology and Radiation Protection, 29, 1-11.

Vukašinović, I., Todorović, D., Životić, L., Kaluđerović, L., & Đorđević, A. (2018). An analysis of naturally occurring radionuclides and 137Cs in the soils of urban areas using gamma-ray spectrometry. International Journal of Environmental Science and Technology, 15, 1049-1060.

Vicić, D., Stoiljkovic, M., Bojat, N., Sabovljevic, M., & Stevanović, B. (2014). Physiological tolerance mechanisms of serpentine tolerant plants from Serbia. Revue d Ecologie, 69 (3-4), 185-195.

Received: xxxxxxx xx, 2019

Accepted: xxxxxxx xx, 2020

PRIRODNI I PROIZVEDENI RADIONUKLIDI U ZEMLJIŠTU PLANINSKIH REGIONA REPUBLIKE SRBIJE I PARAMETRI RADIJACIONOG RIZIKA

Branislava M. Mitrović1*, Dragana Todorović2,

Jelena Ajtić1 i Borjana Vranješ1

1Univerzitet u Beogradu, Fakultet veterinarske medicine,

Bulevar oslobođenja 18, Beograd, Srbija

2Univerzitet u Beogradu, Institut za nuklearne nauke “Vinča”, Laboratorija za zaštitu od zračenja i zaštitu životne sredine, Beograd, Srbija

R e z i m e

U radu su prikazani rezultati gamaspektrometrijskog određivanja sadržaja prirodnih (40K, 238U, 226Ra i 232Th) i proizvedenog (137Cs) radionuklida u zemljištu sa područja planina Maljen, Tara i Kopaonik. Uzorci zemljišta prikupljeni su u periodu od 2002. do 2015. godine na različitim nadmorskim visinama. Na osnovu sadržaja radionuklida u zemljištu odredili smo parametre radijacionog rizika: radijum ekvivalentnu aktivnost, jačinu doze, godišnju efektivnu dozu spoljašnjeg zračenja, indeks spoljašnjeg hazarda, godišnju gonadnu dozu i faktor rizika pojave kancera na području planinskih regiona Republike Srbije, i potom ih uporedili sa ranije objavljenim rezultatima za pojedine regione Republike Srbije.

Ključne reči: zemljište, radionuklidi, gama spektrometrija, parametri radijacionog rizika, planinski region.

Primljeno: xx. xxxxx 2019.

Odobreno: xx. xxxxxx 2020.

# Footnotes

Corresponding author e-mail: slavatab@vet.bg.ac.rs

*Corresponding author e-mail: slavatab@vet.bg.ac.rs